## Slide 1
Transceivers for Wireless Sensor Networks (WSN) & IoT
Σωκράτης Κοσέογλου
Ηλιάνα Δανιηλίδου
Τηλεπικοινωνιακή Ηλεκτρονική Εαρινό Εξάμηνο 2020-2021

## Slide 2
ΙοΤ-WSN Basic Principles/ History/Wireless Technologies
A 4-GHz Low Power, Multi-User Approximate Zero-IF FM-UWB Transceiver for IoT
A Low-Power 2.4GHz ZigBee Transceiver with Inductor-less RF Front-end for IoT applications
Implementing IoT/WSN based smart Saskatchewan Healthcare System

## Slide 3
Transceivers for Wireless Sensor Networks (WSN) & IoT
What is IoT?
1
Internet of Things (IoT) is a system of devices connected to the Internet with the ability to collect and exchange data from users or environment with no human intervention.

## Slide 4
2
Transceivers for Wireless Sensor Networks (WSN) & IoT
Wireless sensor network (WSN) refers to spatially dispersed and dedicated sensors that monitor and record the physical conditions of the environment and forward the collected data to a central location
What is Wireless-Sensor-Network (WSN) ?

## Slide 5
Transceivers for Wireless Sensor Networks (WSN) & IoT
3
IoT Historic Timeline
1982: Carnegie-Mellon researchers connect a vending machine to the Internet so they can remotely check for cold sodas.
1999: The term “Internet of Things” is first used by Kevin Ashton of MIT.
2000: LG announces the first smart fridge.
2008: The first international IoT Conference is held.
Some Important Dates

## Slide 6
4
Transceivers for Wireless Sensor Networks (WSN) & IoT
IoT Wireless Technologies
LPWAN (Low Power Wide Area Networks)
Cellular (4G/5G)
Zigbee
Bluetooth & BLE (Bluetooth Low Energy)
WiFi
RFID

## Slide 7
A 4-GHz Low Power, Multi-User Approximate Zero-IF FM-UWB Transceiver for IoT
ΙοΤ-WSN Basic Principles/ History/Wireless Technologies

## Slide 8
A 4-GHz Low Power, Multi-User Approximate Zero-IF FM-UWB Transceiver for IoT
Introduction
5
Wireless traffic is increased, leading to congestion in commonly used bands
For short-range applications, Ultra-Wideband (UWB) Transceivers solve this problem
Lower Power Spectral Density (PSD)
Types of UWB Transceivers
Impulse Radio Ultra-Wideband (IR-UWB)
Frequency Modulated Ultra-Wideband (IR-UWB)

## Slide 9
6
Frequency Modulated Ultra-Wideband (FM-UWB)
A 4-GHz Low Power, Multi-User Approximate Zero-IF FM-UWB Transceiver for IoT
FM-UWB Modulation Principle
Modulation is achieved in two steps
Input data are modulated onto triangular FSK sub-carrier (SC)
Then, the SC signal drives the Voltage-Controlled Oscillator (VCO)

## Slide 10
FM-UWB Transceiver General Architecture
7
A 4-GHz Low Power, Multi-User Approximate Zero-IF FM-UWB Transceiver for IoT
FM-UWB Transceiver Block Diagram
Both for the Modulation & Demodulation, a Ring Oscillator is used instead of Frequency Synthesizer
1 Transmitter & 2 Receivers
Low Power (LP Rx)
Multi-User (MU Rx)
Tx bit is converter in triangular FSK sub-carrier (SC)
Then the DAC converter drives the Ring Oscillator
Both for the transmitter & the receivers share a single RF IO pad
Tx Transmitter
Power Amplifier (PA) to amplify the signal
Calibration is done using a Frequency-Locked Loop (FLL)

## Slide 11
8
FM-UWB Transceiver General Architecture
A 4-GHz Low Power, Multi-User Approximate Zero-IF FM-UWB Transceiver for IoT
FM-UWB Transceiver Block Diagram
Ring Oscillator for down-conversion of the signal
Active Mixer, instead of LNA
Then, the signal is amplified via an Intermediate Frequency Amplifier (IFA), before demodulation
MU Receiver
Targets better performance (throughput, latency)
Uses Quadrature Down Conversion & baseband delay-line demodulator
Good FM-AM Linearity
LP Receiver
Simplifies the receiver architecture/Low Power Consumption
The SC frequency doubles
Single Down-Conversion branch is used

## Slide 12
FM-UWB Demodulation Principle
9
A 4-GHz Low Power, Multi-User Approximate Zero-IF FM-UWB Transceiver for IoT
FM to AM Demodulation
The MU Receiver demodulates well the Sub-Carrier (SC) signal
While the LP Receiver doubles the Sub-Carrier (SC) signal
MU Receiver spans from 1.15 MHz to 2.3 MHz
LP Receiver has only one SC signal due to high non-linearity of FM-AM Conversion
SC Frequency Plan
4 SC Channels for 100 kbps
200 kHz Bandwidth and 100 kHz Spacing

## Slide 13
10
Transmitter Implementation
A 4-GHz Low Power, Multi-User Approximate Zero-IF FM-UWB Transceiver for IoT
The SC-DDS provides a 6-bit signal
Static DAC provides a current that determines the maximum frequency
Transmitter Transistor-Level Schematic
Sub-Carrier DAC produces the modulated RF FM-UWB signal
The bias current controls the Ring Oscillator
Three-stage Ring Oscillator, each stage is scaled with increasing transistors
Two inverters for isolation between the RO and the PA
Class AB Power Amplifier is used

## Slide 14
A 4-GHz Low Power, Multi-User Approximate Zero-IF FM-UWB Transceiver for IoT
Receiver Implementation
RF Front End and LO generation of the MU Receiver
RF Front End and LO generation of the LP Receiver
M1 Transistor provides voltage-to-current conversion (it can be seen as an LNA)
Two-stage differential ring oscillator to generate quadrature LO signals
Active Mixer has a single LO input
The Local Oscillator (LO) consists of three inverters
The three generated phases are then combined in an edge combiner in order to triple the output frequency
11

## Slide 15
IFA (Intermediate Frequency Amplifier)
A 4-GHz Low Power, Multi-User Approximate Zero-IF FM-UWB Transceiver for IoT
Both receivers have an IFA, three stage Amplifier (each stage is implemented as a feedback Cherry-Hooper Amplifier)
IF Three Stage Amplifier
IFA Gain Characteristic & Noise Figure
The capacitor C1 provides the high-pass part of the characteristic
12

## Slide 16
A 4-GHz Low Power, Multi-User Approximate Zero-IF FM-UWB Transceiver for IoT
FM Demodulator
FM Demodulator of LP Receiver
FM Demodulator of MU Receiver
Standard double balanced mixer
The signal is mixed with itself and the level shifters adjust the DC value of the input signal for the two inputs of the mixer
A similar circuit is used for the MU Receiver, except that here we have two mixers
Load of both demodulators is less than 20μA (usually 3mA)
13

## Slide 17
N-Path Filter
A 4-GHz Low Power, Multi-User Approximate Zero-IF FM-UWB Transceiver for IoT
FM-UWB Transceiver Block Diagram
N-Path Filter Circuit Schematic
MU Receiver supports up to 4 channels
Unwanted channels must be filtered before demodulation
N-Path Filters are good candidates, because of wide tuning and no additional off-chip components
14
Low Pass Filter -> Bandpass Filter
4th Order Type-1 Chebychev Filter
Two biquadratic sections
Each has the following transfer function
b

## Slide 18
A 4-GHz Low Power, Multi-User Approximate Zero-IF FM-UWB Transceiver for IoT
Measurement Results
Die Size is 2.25mm x 2.25mm
The transceiver occupies roughly one-third of the die area
Transmit mode -> S11 close to -8dBm
Receive mode -> S11 less than -10dBm (from 3.6G Hz to 4.8 GHz)
Die Photograph
S11 parameter measurement
15

## Slide 19
A 4-GHz Low Power, Multi-User Approximate Zero-IF FM-UWB Transceiver for IoT
Output Power & Efficiency of the Power Amplifier
Output Power is slightly less than simulated
As a result, the efficiency also drops to peak value of about 21%
The achieved transmitter efficiency (output power / total power consumption) of 12.4% is better than any state-of-the-art.
Measurement Results
Comparison with State-of-the-art
[9] & [10] occupy less die area but require external components
[34] achieves good FM-AM linearity and can support multiple users but these features are not implemented in the chip itself
16

## Slide 20
A 4-GHz Low Power, Multi-User Approximate Zero-IF FM-UWB Transceiver for IoT
A Low-Power 2.4GHz ZigBee Transceiver with Inductor-less RF Front-end for IoT applications
ΙοΤ-WSN Basic Principles/ History/Wireless Technologies

## Slide 21
Transceivers for Wireless Sensor Networks (WSN) & IoT
2.4GHz ZigBee Tranceiver
18
Architecture of the proposed ZigBee Transceiver
ZigBee Technology -> one of the best candidates for the wireless sensor network and Internet of Things (IoT)
the inductor’s size doesn’t scale with the CMOS process, which consumes large chip area and dedicated thick-metal layers
=>
eliminating inductors from the RF front-end, while maintaining low-noise, high-linearity, and high efficiency transmission
Consists of a sliding FS with low-frequency running VCO and self-mixing LO generation, which achieves low power consumption and avoids frequency pulling from the transmitting PA.
The proposed transceiver is implemented in an 180nm CMOS and tested by cooperating with the digital baseband.

## Slide 22
19
Transceivers for Wireless Sensor Networks (WSN) & IoT
Inductor-less LNA
Schematics of the traditional and the proposed CG-CS LNA, as well as the simulated NF, S11 and gain.
Simulation results show that the LNA achieves 2.3dB noise figure, 19.5dB voltage gain while dissipating 1.8mA current at 2.4GHz frequency band.

## Slide 23
Transceivers for Wireless Sensor Networks (WSN) & IoT
Inductor-less Power Amplifier
20
Two-stage inductor-less PA with power control.
A two-stage topology is adopted, in which the pre-driver features 200uA-4mA (20x) tuning range, while the PA stage has 1-8mA (8x) tuning range. The overall PA output power range covers from - 30dBm to +8dBm, which is break down into the two stages.

## Slide 24
21
Transceivers for Wireless Sensor Networks (WSN) & IoT
Frequency Synthesizer with 2/3LO frequency VCO
Frequency Synthesizer simplified block diagram.
The FS generates low phase noise local oscillator (LO) signals for the RX down-conversion and the TX upconversion, covering a 2.4~2.5GHz frequency range.
There are two design issues in the FS, respectively the frequency pulling by the large PA output and the power consumption.
VCO -> oscillate at a different frequency than the PA output

## Slide 25
Transceivers for Wireless Sensor Networks (WSN) & IoT
22
Measurement Results
Die-photo of the ZigBee transceiver.
Input impedance matching of the RF front-end.
Input Matching

## Slide 26
23
Transceivers for Wireless Sensor Networks (WSN) & IoT
Measurement Results
Reconstructed analog output of the receiver.
RX Sensitivity
Frequency Synthesizer
Measured synthesizer phase noise at 2.44GHz.
NF=Pin-10logBW-SNRout+174

## Slide 27
Transceivers for Wireless Sensor Networks (WSN) & IoT
Measurement Results
24
Measured TX output spectrum, constellation and EVM.
TX Transmission
Τhe measured OQPSK output power, constellation diagram and EVM.
The TX’s EVM is measured at 4%, while outputting 7.6dBm power.

## Slide 28
A 4-GHz Low Power, Multi-User Approximate Zero-IF FM-UWB Transceiver for IoT
A Low-Power 2.4GHz ZigBee Transceiver with Inductor-less RF Front-end for IoT applications
Implementing IoT/WSN based smart Saskatchewan Healthcare System
ΙοΤ-WSN Basic Principles/ History/Wireless Technologies

## Slide 29
26
Transceivers for Wireless Sensor Networks (WSN) & IoT
Smart Saskatchewan Healthcare System
Smart Saskatchewan Healthcare System architecture
Saskatchewan health region network nodes

## Slide 30
27
Transceivers for Wireless Sensor Networks (WSN) & IoT
Hierarchical and location-based WSN routing
IoT health solution/system framework

## Slide 31
28
Transceivers for Wireless Sensor Networks (WSN) & IoT
Clinical environment interaction in smart system
IoT smart Saskatchewan healthcare services and applications

## Slide 32
29
Transceivers for Wireless Sensor Networks (WSN) & IoT
Full mesh smart Saskatchewan Healthcare System

## Slide 33
30
Transceivers for Wireless Sensor Networks (WSN) & IoT
Βιβλιογραφία
  Vladimir Kopta, Christian C. Enz, “A 4-GHz Low-Power, Multi-User Approximate Zero-IF FM-UWB Transceiver for IoT”, IEEE JOURNAL OF SOLID-STATE CIRCUITS, VOL. 54, NO. 9, SEPTEMBER 2019
Bing Xia, Nan Qi, Liyuan Liu and Nanjian Wu, “A Low-Power 2.4GHz ZigBee Transceiver with Inductor-less RF Front-end for IoT applications”, 978-1-5090-6389-5/17/$31.00 ©2017 IEEE
  Adeniyi Onasanya, Sari Lakkis, Maher Elshakankiri, “Implementing IoT/WSN based smart Saskatchewan Healthcare System”, Publiced Online: 02 January 2019

## Slide 34
Thank you for your time!
Questions?